## Slide 1: RISCV with floating Point
SUBMITTED BY :
AbdelRahman Atef Eid Yassin
Mahmoud Mohamed Taha
Ahmed Khattab Mahmoud Khattab

## Slide 2: OUTLINES
OBJECTIVE
Instruction Set Architecture
IEEE Floating point Standard
Floating Point Unit Design
Integrating With RISCV
  Floating Point System
  Connection with RISC V
Testing and Results
References

## Slide 3: OBJECTIVE
The aim of this is project is to extend RISC V processor to be able to deal with floating point instructions .
STEPS
  1- Instruction Set Architecture study
  2- Design FPU unit that deals with floating point numbers
  3- Integrate it with RISC V
ISA study
Design FPU
RISC V
Integration

## Slide 4: Instruction set ARCHITECTURE
31-25 | 24-20 | 19-15 | 14-12 | 11-7 | 6-0 | Instruction | illustration
Imm[11:0] |  | rs1 | 010 | rd | 0000111 | FLW | Load a value from location rs1 (integer reg) + imm to rd (float reg)
Imm[11:5] | rs2 | rs1 | rm | Imm[4:0] | 0100111 | FSW | store a value from rs2 (float reg) +memory( imm + rs1)
0000000 | rs2 | rs1 | rm | rd | 1010011 | FADD | Rd = r1 + r2 all float registers
0000100 | rs2 | rs1 | rm | rd | 1010011 | FSUB | Rd = r1 - r2
0001000 | rs2 | rs1 | rm | rd | 1010011 | FMUL | Rd = r1 * r2
0010100 | rs2 | rs1 | 000 | rd | 1010011 | FMIN | Rd = min (rs1,rs2)
0010100 | rs2 | rs1 | 001 | rd | 1010011 | FMAX | Rd = max (rs1,rs2)
1100000 | 00000 | rs1 | rm | rd | 1010011 | FCVT.W.S | Convert float in rs1(float) to integer in rd(integer)
1101000 | 00000 | rs1 | rm | rd | 1010011 | FCVT.S.W | Convert int in rs1 (int) to float in rd(float)
1110000 | 00000 | rs1 | 000 | rd | 1010011 | FMV.X.W | Move float number from rs1 (float) to rd (integer)
1111000 | 00000 | rs1 | 000 | rd | 1010011 | FMV.W.X | Move int number from rs1 (int) to rd (float)
1010000 | rs2 | rs1 | 010 | rd | 1010011 | FEQ.S | Rd = 1 (integer) if rs1 == rs2 (float)
1010000 | rs2 | rs1 | 001 | rd | 1010011 | FLT.S | Rd = 1 (integer) if rs1 < rs2 (float)
1010000 | rs2 | rs1 | 000 | rd | 1010011 | FLE.S | Rd = 1 (integer) if rs1 <= rs2 (float)
1110000 | 00000 | rs1 | 001 | rd | 1010011 | FCLASS.S | Classify floating point

## Slide 5: IEEE 754 floating Point Standard
Sign
S=0 (Positive)
S=1 (Negative)
Number is presented as
-9.75 > - 1001.11 = - 1.00111 x 2^3
S= 1
E= 127 + 3 = 130 = 1000 0010
F = 00111 00….00
Floating numbers
+0,-0
+INF,-INF
normalized
denormalized
0<e<255
e=0
F!=0
e=0
F=0
nan
e=255
F=0
e=255
F!=0
For a normalized number, the 1 of 1. f is not stored in the 32-bit data; it is called a hidden bit. For a
denormalized number, the hidden bit is a 0.

## Slide 6: Top level
The floating point co-processor will accepts input signals as three input
1- operands (single precision)
2- opcode
3- round mode.
It decodes instructions and executes them

## Slide 7: Floating point unit
ADD/SUB
F2I
I2F
FMUL
Compare
Min/Max
Classify
FDIV
FSQRT
FPU_decode[3:0]
A[31:0]
Frm[2:0]
sub
B[31:0]
a
b
frm
sub
R1
R2
R3
R4
R5
R6
R7
R8
R9
R1
R2
R3
R4
R5
R6
R7
R8
R9
result[31:0]
NV1
OF1
UF1
NX1
NV2
OF2
UF2
NX2
a
a
a
b
frm
a
b
frm
a
b
frm
a
frm
NV3
NX3
UF3
NV4
OF4
UF4
NX4
NV5
NV6
DZ
Invalid
OF
UF
NX
NV1
NV2
NV3
NV4
NV5
NV6
OF1
OF2
OF4
UF1
UF2
UF3
UF4
NX1
NX2
NX4
NX6
NX3
NX5
FPU_decode[3:0]
FPU Floating Point Unit is implemented as top module in FPU.v

## Slide 8: Float to integer
Calculate hidden bit and determine if mantissa is not zero
Determine if number is denormalized or zero
Determine the sign
Put hidden bit at left then 23 bits of f then Shift right by 158 – e
If there is a value at least 23 bits there is precision loss
If sign is negative ,takes two’s complement
Output UF =1 if it is denormalized or precision lost
Output OF =1 if a value more than 32 bits
Output invalid in case invalid conversion of a bigger result
A 32-bit single-precision floating-point number has a much wider range than the integer.
This means that many floating-point numbers cannot be converted to integer correctly
hb
f
zeros
1bit
32 bits
23 bits
Shift right by 127+31 - e
Rounding mode | meaning
000 | RNE
001 | RTZ
010 | RDN
011 | RUP
100 | RMM

## Slide 9: Integer to float
Shift the point by 31 bits
Normalize to 1.xx format
Calculate shift amount
Determine the sign
Calculate exponent =158-sa
Output invalid flags if some values are thrown away by shift

## Slide 10: Floating point addition and subtraction
1- determine who is largest a or b
2- make exponent equal by shifting the smallest one (difference between exponents)
3- add them together according to add or sub
4- normalize result
5- rounding result (least 5 bits 01 101) grs = 01 1
g is guard bit ,r is rounding bit , s is sticky bit (or last 3bits)
6- normalize again after rounding (adding 1)
7- if exponent reaches max value it is overflow

## Slide 11: ROUNDING

## Slide 12: Floating point addition and subtraction

## Slide 13: Floating Multiplier
1- exponent of result is addition of both exp + bias
2- sign of result is xor of both
3- multiply the fractions together (Wallace tree)
Hidden bit + 23 bit by Hidden bit + 23 bit
4- normalize result
6- rounding (takes only 23 bits according to same rounding function

## Slide 14: Float multiplier

## Slide 15: Wallace tree multiplier

## Slide 16: Check sign

## Slide 17: Comparison
Check exponent and mantissa to be zeros or all ones
Determine if any of number is nan or invalid
If numbers are valid, compare the numbers
rm | output
10 (equality) | =1 when a == b (sign ,exp,mantissa)
01 (less than) | Check if different signs if a is - ,output = 1 If same sign , output = 1 when exp(a) < exp (b) and if equal check mantissa
00 (less than or equal) | Check if different signs if a is - ,output = 1 If same sign , output = 1 when exp(a) <= exp (b) and if equal check mantissa

## Slide 18: Min max
Check exponent and mantissa to be zeros or all ones
Determine if any of number is nan or invalid
If numbers are valid, compare the numbers
rm | output
0 (min) | Check sign if different signs ,output is the negative number If same sign output operand with the least exponent If same exponent output operand with the least mantissa
1 (max) | Check sign if different signs ,output is the positive number If same sign output operand with the largest exponent If same exponent output operand with the largest mantissa
Invalid

## Slide 19: Classify
Quiet nan if exponent all ones and mantissa has a leading zero and any one
Signaling nan if exponent all ones and mantissa has a leading one
Normal number has one in bit 23 of mantissa ,subnormal has zero

## Slide 20: FPU DECODER
Funct7 7bits | Fpu decode | rm | Mov from f reg | Mov from i reg | Freg_write | Integer_reg_write | Mov_from_float_result | Mov int to fpu | Instruction
0000000 | 0000 | X | 0 | 0 | 1 | 0 | 0 | 0 | Add
0000100 | 0000 | X | 0 | 0 | 1 | 0 | 0 | 0 | Sub
1100000 | 0001 | X | 0 | 0 | 0 | 1 | 1 | 0 | f2i
1101000 | 0010 | X | 0 | 0 | 1 | 0 | 0 | 1 | i2f
0001000 | 0011 | X | 0 | 0 | 1 | 0 | 0 | 0 | mul
1010000 | 0100 | X | 0 | 0 | 0 | 1 | 1 | 0 | compare
0010100 | 0101 | X | 0 | 0 | 1 | 0 | 0 | 0 | minmax
1110000 | 0110 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | classify
1110000 | 1111 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | Move float to int
1111000 | 1111 | X | 0 | 1 | 1 | 0 | 0 | 0 | Mov int to float
Write enable of freq and integer reg
Data out from
fpu to int reg
Data out from
int reg needed as operand to fpu

## Slide 21: Floating point system

## Slide 22: RISC V edited
The Main Decoder of RISC V is edited so the control unit to allow Float instructions
Main Decoder
float_RegWrite
float_store
fpu_decoder_en
ResultSrc_float
Instr[6:0]
Opcode | Instruction | float_RegWrite | float_store | fpu_decoder_en | ResultSrc_float
0000111 | load | 1 | 0 | 0 | 1
0100111 | store | 0 | 1 | 0 | 0
1010011 | Rest of RISCV 32F | 0 | 0 | 1 | 0

## Slide 23: RISC V edited

## Slide 24: Testing Instructions
Instructions | Initial values | Expected Output
Sw $f1,4($x1) | X1 = 4 , memory[2] =2,$f1=2.5 | Memory[2]=2.5
Lw $f25,4($x1) | $f25= 1124.53 | $f25=2.5
Add $f3,$f1,$f2 | $f1=2.5 $f2=2.6 | $f3=5.1
Sub $f31,$f16,$f15 | $f16=4.75 $f15=2.25 | $f31=2.5
MUL $f28,$f1,$f4 | $f1=2.5 ,$f4=-3.5 | $f28 = -8.75
MIN $f30,$f28,$f29 | $f28=-8.75 $f29=10500.5 | $f30 = -8.75
MAX $f30,$28,$f29 | $f28=-8.75 $f29=10500.5 | $f30 = 10500.5
F2i $x5,$f17 | $f17 =2.147483520*10^9 (4eff ffff) | $x5=2147483520(7fffff80)
I2f $f26,$x1 | $x1 = 4 | $f26=4.0
Mov $x8,$f12 | $f12 = 0000ffff | $x8 = 0000ffff
Mov $f25,$x7 | $x7 = 0000 0028 h | $f25 = 0000 00028 h
FEQ $x2,$f21,$f21 | $f21 = 530.125 | $x2=1
FLT $x3,$f3,$f2 | $f3= 5.1 $f2 =2.6 | $x3=0
FLE $x4,$f3,$f2 | $f3= 5.1 $f2 =2.6 | $x3=0
FCLASS $x10,$f9 | $f9 = +INF | $x10 =0000 0080

## Slide 25: Testing store instruction

## Slide 26: Testing load instruction

## Slide 27: Testing ADD Instruction

## Slide 28: TESTING SUB INSTRUCTION

## Slide 29: Testing mul instruction

## Slide 30: Testing Min & MAX

## Slide 31: TESTING F2I

## Slide 32: TESTING I2F

## Slide 33: Testing mov instructions

## Slide 34: TESTING COMPARE INSTRUCTIONS

## Slide 35: TESTING CLASSIFY

## Slide 36: References
The RISC-V Instruction Set ManualVolume I: User-Level ISADocument Version 2.2Editors: Andrew Waterman1, Krste Asanovic1;21SiFive Inc.,2CS Division, EECS Department, University of California, Berkeleyandrew@sifive.com, krste@berkeley.eduMay 7, 2017
COMPUTERPRINCIPLESAND DESIGN IN VERILOG HDL Yamin LiHosei University, Japan
https://www.slideshare.net/prochwani95/06-floating-point